Name of journal: World Journal of Gastrointestinal Endoscopy

ESPS Manuscript NO: 15790

Columns: Letter to the Editor

Toward an easier indigocarmine chromoendoscopy

Barret M et al. Indigocarmine chromoendoscopy

Maximilien Barret, Marine Camus, Sarah Leblanc, Romain Coriat, Frédéric Prat, Stanislas Chaussade

Maximilien Barret, Marine Camus, Sarah Leblanc, Romain Coriat, Frédéric Prat, Stanislas Chaussade, Gastroenterology Department, Cochin Hospital, 75014 Paris, France

Maximilien Barret, Marine Camus, Sarah Leblanc, Romain Coriat, Frédéric Prat, Stanislas Chaussade, Medical School, Paris Descartes University, 75006 Paris, France

Author contributions: Barret M drafted the manuscript; Camus M, Leblanc S and Coriat R performed the endoscopic procedures; Prat F corrected the manuscript; Chaussade S performed the endoscopic procedures and designed the study; all authors approved the final version of the manuscript.

Conflict-of-interest: None.

Open-Access: This article is an open-access article which was selected by an in-house editor and fully peer-reviewed by external reviewers. It is distributed in accordance with the Creative Commons Attribution Non Commercial (CC BY-NC 4.0) license, which permits others to distribute, remix, adapt, build upon this work non-commercially, and license their derivative works on different terms, provided the original work is properly cited and the use is non-commercial. See: http://creativecommons.org/licenses/by-nc/4.0/

Correspondence to: Maximilien Barret, MD, MSc, Gastroenterology Department, Cochin Hospital, 27 Rue du Faubourg St Jacques, 75014 Paris, France. maximilien.barret@cch.aphp.fr

Telephone: +33-1-58411967

Fax: +33-1-79724571

Received: December 9, 2014

Peer-review started: December 9, 2014

First decision: January 8, 2015

Revised: April 13, 2015

Accepted: April 27, 2015

Article in press:

Published online:

Abstract

Indigocarmine chromoendoscopy has been proven to improve the detection of colonic lesions during screening colonoscopy, and is associated with increased adenoma detection rates. Furthermore, it is commonly used to help in the delineation and characterization of colorectal neoplasms. However, it usually requires the use of a spraying catheter that decreases the suction capacity of the endoscope, and is time- consuming. Herein, we report on the feasibility of indigo carmine chromoendoscopy during colonoscopy without using a spraying catheter, with the dye being administered through the air/water channel of the endoscope. Since the suction channel remains free, the air can be exsufflated and the staining then applies uniformly onto the colonic walls with the excess indigocarmine dye being immediately eliminated. In our experience with various types of colonoscopes and cap-assisted colonoscopy, this procedure makes indigocarmine chromoendoscopy much easier and quicker to perform, and might save the use of a spray catheter.

Key words: Indigocarmine; Chromoendoscopy; Colonoscopy; Adenoma detection rate; Colorectal cancer screening

© The Author(s) 2015. Published by Baishideng Publishing Group Inc. All rights reserved.

Core tip: We report on the feasibility of indigocarmine chromoendoscopy during colonoscopy without using a spraying catheter, with the dye being administered through the air/water channel of the endoscope.

Barret M, Camus M, Leblanc S, Coriat R, Prat F, Chaussade S. Toward an easier indigocarmine chromoendoscopy. World J Gastrointest Endosc 2015; In press

TO THE EDITOR

Indigocarmine chromoendoscopy has proven useful in increasing the overall diagnostic yield of colonoscopy and the adenoma detection rate[1]. This technique is currently recommended in routine colorectal cancer screening in patients with long-standing inflammatory colitis or hereditary nonpolyposis colorectal cancer[2]. The standard technique implies pancolonic spraying with 0.2% indigocarmine delivered through a spraying catheter inserted in the accessory channel of the colonoscope. Spraying is performed segmentally during withdrawal of the endoscope and excess dye is suctioned before mucosal examination.

However, the use of a spray catheter has a certain cost, limits the suction capacity of the endoscope and often requires several passages with the endoscope, which can sometimes be difficult in some patients. We report on the feasibility of the indigocarmine dye application directly through the colonoscope air/water channel. Upon cecal intubation, the indigo carmine solution is prepared in the water bottle, using two 10 mL vials of 1% indigocarmine diluted in 80 mL of water, in order to obtain the 0.2% concentration (Figure 1). The indigocarmine dye is delivered by pressing on the air/water valve while orienting the head of the endoscope against the colonic walls and withdrawing the colonoscope. The indigocamine dye application is shown on Figure 2. It should be noted that the indigocarmine stained water does not remain on the objective lens of the endoscope rendering clear water unnecessary for the cleaning of the tip of the endoscope during the chromoendoscopic procedure. Once the end of a colonic segment has been reached, suction of the air allows uniform application of the dye on the mucosa and elimination of excess fluid. New air insufflation is then needed for the colonic mucosal examination. Immediately after the procedure, the air/water channel of the endoscope is flushed with water from another water bottle until the outflow is clear, to make sure that no indigocarmine dye remains inside the channel. After standard washing, we did not observe any residual staining in the water bottles. Our preliminary experience with 15 patients suggests that this simplified indigocarmine chromoendoscopic technique is feasible with Olympus® or Fujifilm® colonoscopes, with or without a cap (Figures 3-5) and with a median withdrawal time of 21 ± 12 min.

# REFERENCES

1 Kahi CJ, Anderson JC, Waxman I, Kessler WR, Imperiale TF, Li X, Rex DK. High-definition chromocolonoscopy vs. high-definition white light colonoscopy for average-risk colorectal cancer screening. Am J Gastroenterol 2010; 105: 1301-1307 [PMID: 20179689 DOI: 10.1038/ajg.2010.51]

2 Kamiński MF, Hassan C, Bisschops R, Pohl J, Pellisé M, Dekker E, Ignjatovic-Wilson A, Hoffman A, Longcroft-Wheaton G, Heresbach D, Dumonceau JM, East JE. Advanced imaging for detection and differentiation of colorectal neoplasia: European Society of Gastrointestinal Endoscopy (ESGE) Guideline. Endoscopy 2014; 46: 435-449 [PMID: 24639382 DOI: 10.1055/s-0034-1365348]

P- Reviewer: Amornyotin S, Garcia AZG, Kikuchi H S- Editor: Gong XM

L- Editor: E- Editor:

# Figure 1 0.2% indigocarmine solution prepared in the water bottle.

# Figure 2 Indigocarmine dye application through the air/water channel of the endoscope.

# Figure 3 Endoscopic view of the colonic mucosa after indigocarmine staining using a Fujifilm® colonoscope.

# Figure 4 Endoscopic view of the colonic mucosa after indigocarmine staining using an Olympus® colonoscope and a cap.

# Figure 5 Endoscopic view of a sessile serrated adenoma after indigocarmine staining.