Name of journal: World Journal of Gastroenterology

ESPS Manuscript NO: 3398

Columns: Minireviews

Endoscopy and polyps-diagnostic and therapeutic advances in management

Steele  SR et al. Endoscopy and polyps

Scott R Steele, Eric K Johnson, Bradley Champagne, Brad Davis, Sang Lee, David Rivadeneira, Howard Ross, Justin A Maykel

Scott R Steele, Eric K Johnson, Department of Surgery, Madigan Army Medical System, Madigan Health System, Tacoma, WA 98431, United States

Bradley Champagne, Division of Colon and Rectal Surgery, Case Western Reserve Medical Center, Cleveland, OH 44106, United States

Brad Davis, Department of Surgery, University of Cincinnati, Cincinnati, OH 45267, United States

Sang Lee, Division of Colon and Rectal Surgery, Weill Cornell Medical College, New York, NY 10065, United States

David Rivadeneira, Department of Surgery, Huntington Hospital/North Shore-LIJ Health System, Huntington, NY 11743, United States

Howard Ross, Department of Surgery, Riverview Plaza Riverview Medical Center, Red Bank, NJ 07701, United States

Justin A Maykel, Division of Colon and Rectal Surgery, University of Massachusetts Memorial Medical Center, Worcester, MA 01609, United States

Author contributions: Steele SR contributed to conception and design, and drafting of manuscript; Steele SR and Johnson EK contributed to acquisition of data; Steele SR, Johnson EK, Champagne B, Davis B, and Maykel JA contributed to analysis and interpretation of data; Johnson EK, Champagne B, Davis B, Lee S, Rivadeneira D, Ross H, and Maykel JA contributed to critical revision; Steele SR and Maykel JA contributed to supervision.

Correspondence to: Scott R Steele, MD, FACS, Chief, Colon and Rectal Surgery, Department of Surgery, Madigan Army Medical Center, 9040a Fitzsimmons Drive, Fort Lewis, WA 98431, United States. harkersteele@mac.com

Telephone: +1-253-9682200  Fax: +1-253-9685900

Received: Revised:

Accepted: June 8, 2013

Published online:

Abstract

Despite multiple efforts aimed at early detection through screening, colon cancer remains the third leading cause of cancer-related deaths in the United States, with an estimated 51000 deaths during 2013 alone. The goal remains to identify and remove benign neoplastic polyps prior to becoming invasive cancers. Polypoid lesions of the colon vary widely from hyperplastic, hamartomatous and inflammatory to neoplastic adenomatous growths. Although these lesions are all benign, they are common, with up to one-quarter of patients over 60 years old will develop pre-malignant adenomatous polyps. Colonoscopy is the most effective screening tool to detect polyps and colon cancer, although several studies have demonstrated missed polyp rates from 6%-29%, largely due to variations in polyp size. This number can be as high as 40%, even with advanced (> 1 cm) adenomas. Other factors including sub-optimal bowel preparation, experience of the endoscopist, and patient anatomical variations all affect the detection rate. Additional challenges in decision-making exist when dealing with more advanced, and typically larger, polyps that have traditionally required formal resection. In this brief review, we will explore the recent advances in polyp detection and therapeutic options.

Keywords: Polyps; Endoscopy; Colonoscopy; Endoscopic submucosal dissection; Endoscopic mucosal resection; Quality; Combined endoscopic-laparoscopic resection; Combined laparoscopic-endoscopic resection; Combined endoscopic-laparoscopic surgery

Core tip: Changes in polyp detection including chromoendoscopy and narrow band imaging (NBI), as well as reliance on quality indicators such as the 6-minute withdrawal time, aim to improve adenoma detection rates. Once identified, novel approaches for large and advanced polyps such as endoscopic submucosal dissection (ESD) and endoscopic mucosal resection (EMR), along with combined endoscopic-laparoscopic resection (CLER/CELS) are available to surgeons that may obviate the need for formal resection. Although technical expertise and experience is required, physicians caring for these patients should be familiar with each of these alternative procedures.

Steele SR, Johnson EK, Champagne B, Davis B, Lee S, Rivadeneira D, Ross H, Maykel JA. Endoscopy and polyps-diagnostic and therapeutic advances in management.

Available from: URL:

DOI:

INTRODUCTION

Endoscopic technology has undergone dramatic improvements since Philipp Bozzini (1773-1809), a urologist from Frankfurt, Germany, developed the lichtleiter in 1806--a light-conducting system that featured a candle and system of prisms to inspect the rectum, bladder and esophagus of patients[1]. Since then, multiple different physicians and scientists such as Nitze, Mikulicz, Waye, and Shinya have advanced this technology from a rigid device able to look into the bladder and stomach to a fully flexible endoscope capable of evaluating the entire gastrointestinal tract. Modern endoscopic equipment allows the direct visualization and treatment of many diseases ranging from colorectal polyps, carcinoma, inflammatory bowel disease, intestinal ischemia, diarrhea, diverticular disease, and lower gastrointestinal bleeding. Auxiliary devices ranging from biopsy forceps, snares, injection needles, various knives, baskets and balloon dilators have been developed to expand the ability of surgeons and gastroenterologists alike to manage complex pathology through the use of endoscopes. This update will briefly review some of the emerging advances and evolving parameters as well as their impact on clinical practice.

QUALITY PARAMETERS

Colon cancer remains the third leading cause of cancer-related deaths in the United States when each gender is considered separately and second when combined, with an estimated 50830 deaths in 2013 alone. This is despite multiple efforts aimed at early detection through screening, as well as evidence that routine screening reduces mortality[2-5]. Barriers to screening include patient fear of the exam and results, financial constraints, time off from work, transportation, and (in some regions) access to care. Multiple studies have demonstrated that when compared to flexible sigmoidoscopy and air-contrast barium enemas, colonoscopy is the most effective screening tool to detect colon cancer[6-7]. These dramatic results, in part, prompted Medicare in July 2001 to provide coverage for screening colonoscopy; which, along with technological advances, dramatically increased its overall use in the United States[8]. Despite the success of optical colonoscopy to detect and remove polyps, there remains a substantial rate of undetected polyps. In most major series this rate appears to be low, but has not improved over time, suggesting the need for further advances in the technique. Large studies that include physicians with extensive experience have demonstrated missed polyp rates from 6%-29%, with the variation depending primarily on the size of the lesion[9]. Not surprisingly, missed polyp detection rates have been significantly lower for larger lesions. Pooled analysis of tandem colonoscopies has revealed a failure to detect polyps of any size in as many as 22% of cases (95%CI: 19%-26%). In this systematic review, when further stratified by size, adenoma miss rates were 2.1% lesions for ≥ 1cm, 13% for those 5-10 mm, and 26% for polyps 1-5mm[10]. Others have reported similar results, with miss rates for all polyps at 28%, adenomas (20%), polyps < 5mm (12%), > 5mm (9%) and advanced adenomas (11%)[11]. When accounting for other factors such as the concomitant presence of a sub-optimal bowel preparation, these rates have been reported to be higher than 40% for any size polyp, and even up to 36% with advanced adenomas[12]. In order to understand how we may potentially be able to lower this missed adenoma detection rate, we will explore these factors and the data behind each of them.

Time of withdrawal

One factor that has more recently been identified to impact overall polyp detection rates is colonoscopy withdrawal time. In 2002, a United States Multi-Society Task Force on Colorectal Cancer recommended that the withdrawal time for colonoscopies should average 6-10 min. Interestingly, this was based, in part, on a single small series of only 10 consecutive colonoscopies performed by two experienced endoscopists with vastly different withdrawal practices that found different adenoma missed rates[13]. Following confirmatory studies, practice guidelines have since recommended that endoscopists spend a minimum of 6-10 min examining the colonic mucosa during the withdrawal phase of colonoscopy to optimize the diagnostic yield of polyps. In many instances, this has evolved to become a metric that is tracked by hospital administrators to assess the quality of colonoscopies[14]. The response was initially positive, and adherence to this benchmark was supported by findings in a study by Simmons and colleagues that included 11000 colonoscopies showing a direct association between longer withdrawal times and higher polyp detection rates (r = 0.76; P < 0.0001). Although this association was overall strong, it dropped significantly as polyp size increased (r = 0.19 for polyps 6-9mm; r = 0.28 for polyps 10-19mm, r = 0.02 for polyps ≥ 20mm)[15]. Small variations on this theme were subsequently reported, with others finding overall procedure time (which included the consent and sedation periods and not just withdrawal time) correlated with increased rates of polyp detection (r = 0.64; OR = 1.4, 95%CI: 1.19-1.64 for polyps > 1 cm; OR = 1.03, 95%CI: 0.74-1.43 for polyps > 2cm) [16]. In one of the sentinel papers, Barclay and associates published a study in the NEJM with 7,882 colonoscopies using 6 min as the minimum length of time to allow for “adequate inspection” during withdrawal[17]. In this study of 12 gastroenterologists, rates of polyp detection ranged widely when measured either by number (0.1 - 1.05 mean number per patient) or percentage with adenomas (9.4% - 32.7%), as well as times of withdrawal (3.1 - 16.8 min for procedures with no polyps removed). When specifically using a cutoff of 6 min , those with longer withdrawal times had significantly higher rates of detection for any neoplasia (28.3% vs 11.8%, P < 0.001), as well as advanced lesions (6.4% vs 2.6%, P = 0.005). Since then, multiple authors have confirmed average withdrawal times of 6 min or longer to be correlated with increased adenoma detection rates, including a quality assurance review of 15955 patients over 49 ambulatory centers, 17 states and 315 gastroenterologists, where longer withdrawals had a 1.8-fold higher rate of polyp detection[18]. In this review, factors that were found to be the strongest predictors of withdrawal time ≥ 6 min include the presence of carcinoma (OR = 3.7), adenoma (OR = 2), and number of polyps visualized (OR = 1.7). Whether the study is performed in a private practice or academic environment, the relationship between longer withdrawal times and higher rates of overall polyp detection, or adenomas per patient (0.09-0.82), has been consistent[19].

However, the adoption of this quality indicator has not been uniformly supported nor met with complete agreement. Several authors have demonstrated no difference in polyp detection rates, despite improving the frequency of meeting the >6 minute quality metric from 65% to near 100% of the time[14]. Others argue that colonoscopy rarely misses polyps >1cm (i.e., the most clinically significant polyps), regardless of the time spent during the withdrawal phase. Still others have agreed that while withdrawal time is associated with higher rates of polyp detection, longer withdrawal times have not been associated with changes in rates of neoplasia discovered at subsequent follow-up colonoscopies, including a recent VA Cooperative Studies Group analysis[20]. Similarly, after a monitoring and feedback program was instituted that focused on withdrawal times and polyp detection rates, there was an increase in mean withdrawal time (6.6 to 8.1 min, P < 0.0001) and overall polyp detection rate (33.1% to 38.1%, P = 0.04). However, this was again observed to not be associated with an increase in neoplasia detection rate from the initial to the post-intervention time periods (19.6% to 22.7%; P = 0.17)[21].

Despite this, withdrawal time has evolved into a quality metric indicator in many centers for determining the adequacy of colonoscopy. As such, this has led to some changes in clinical practice--both positive and negative. Some authors have reported improved rates of longer withdrawal times to comply with these guidelines, simply knowing that this quality measure was being recorded, but without using that time to perform the corresponding evaluation. To combat this, practices such as vetting through bystander observation and video recording have been attempted, though without a significant increase in polyp detection[22]. Other authors have shifted their focus in an attempt to further clarify the reasons for variations in polyp detection rate. Factors such as number of procedures, mean patient age, percentage of women, and mean procedure time have all been evaluated (in addition to polyp size) with only procedure time being significantly associated with polyp detection rate in a study of 2,665 screening colonoscopies[23]. Multiple other patient and physician-related factors have also been identified as causes for higher miss rates including experience of the endoscopist, larger colon folds, morphology of polyp, and polyp location (i.e, blind spots at the flexures)[11, 24].

Physician fatigue

Physician fatigue has been considered another variable that affects colonoscopy quality performance and adenoma detection rates. This was first noted in a study demonstrating that afternoon colonoscopies have higher failure rates than morning colonoscopies, with higher overall incompletion rates (6.5% vs 4.1%, P = 0.013) as well as higher rates of inadequate bowel preparation (15.4% in a.m. vs 19.7% in p.m.)[25]. When using cecal intubation rates as the endpoint, success was again lower in the afternoon (93.5% vs 95%, P = 0.02), although gender, age and bowel preparation were felt to play a role in these differences as well[26]. Adenoma detection rates have also varied based on the time of day the colonoscopy is performed, with one study reporting rates of 29.3% in the morning versus 25.3% in the afternoon (P = 0.008), independent of factors such as poor bowel preparation, withdrawal time, or partial evaluation[27]. To further clarify this, authors have compared results of providers that perform a full day of colonoscopy with those limited to half-day blocks. Adenoma detection rates in those only working half days have showed no significant difference between early and late procedures within that time period (27.6% vs 26.6%, OR 1.05; CI 0.88-1.26, P = 0.56), while those in the same practice with full-day blocks reporting higher detection rates in the morning (26.1% vs 21%; P = 0.02), suggesting that the additional time, and subsequent fatigue, plays a role for this difference[28]. It appears that provider fatigue culminates in lack of focus or acumen in many cases, and translates into lower rates of “successful” colonoscopies as time progresses. Interestingly, polyp detection rates have also been shown to decline as time passes during an endoscopist’s schedule, regardless of time of day, or number of prior procedures. Each elapsed hour in their work schedule was associated with a 5.6% reduction in polyp detection (P = 0.005), suggesting that physician fatigue can progress more rapidly in certain cases[29].

Training and technique

Regardless of the metric proposed, proper training remains a major factor in becoming and remaining proficient in any endeavor. Historically, intra-procedural quality indicators for colonoscopy have focused primarily on physician-related factors such as cecal intubation rates, terminal ileal intubation, number of polyps detected, number of polyps retrieved, size of polyps detected, time to reach the cecum, and more recently withdrawal time. Guided by principles such as the United Kingdom Department of Health Global Rating Scale for endoscopy, emphasis has shifted more on defining quality experience through patient-driven metrics including appropriateness of the intervention, proper information/consent, overall safety, patient comfort, and providing timely results[30]. Use of colonoscopy-based virtual-simulator models has been one way to supplement inadequate exposure during residency training, and improve both the trainee experience and end result. Multiple studies have demonstrated that following intervention with 3-D simulators, many of these aforementioned traditional metrics such as cecal intubation rates, overall times, and need for further medication interventions significantly improve[31]. On the other hand, it remains to be seen how these newer quality metrics will be evaluated, reported and enforced.

POLYP CLASSIFICATION

In general terms, a polyp refers to the elevation of tissue above the gastrointestinal epithelium. Colon polyp types range widely from hyperplastic, hamartomatous, and inflammatory varieties to neoplastic adenomatous lesions. Although these lesions are all “benign,” up to one-quarter of patients over 60 years old will have “pre-malignant” adenomatous polyps. Traditionally, polyps have been classified most commonly by their histology (i.e., villous, tubular, tubulovillous, etc.), location, and physical description—with pedunculated and sessile being the most common descriptive classes. Since their first description in 1985[32], flat adenomas are increasingly more common and represent one of the “high-risk” categories along with adenomas larger than 1cm, those with high-grade dysplasia, those associated with IBD, villous or tubulovillous adenomas, and patients with multiple adenomas (typically > 3). Similarly, serrated adenomas represent another high-risk group, and are believed to represent a unique pathway in the adenoma-carcinoma sequence.

Flat polyps and serrated adenomas

While there has been some controversy regarding the impact and importance of flat adenomas in the United States and Europe, they are more widely believed to be significant in Asia. The Japanese Research Society Classification (Kudo classification of adenomas) describes flat lesions as those with a height that is less than one half the diameter[33]; while the Paris classification uses protruding and non-protruding divisions[34]. Increasingly, these lesions are recognized for their role in malignancy as well as difficulty with identification[35]. Serrated polyps represent another type of lesion that has been reported to be more difficult to diagnosis. Originally described following evaluation of hyperplastic polyposis syndrome patients, these lesions have a characteristic serrated architecture and can occur either as a traditional serrated adenoma (classically seen as a polypoid lesion), or as a sessile serrated adenoma (flat, slightly raised, right-sided > left). Though historically often diagnosed as a variant of hyperplastic polyps, these lesions are found in about 7% of all colonoscopies, and are now more properly classified as their own distinct entity. They are also believed to have a higher risk of malignancy that occurs apart from the traditional adenoma to carcinoma sequence[36, 37].

The traditional polyp-cancer sequence has been established since Muto and colleagues described it in 1975[38]. Adenocarcinoma of the colon can arise via multiple different pathways, with the most common described by genetic alterations that result in micro-satellite stable carcinomas[39]. Approximately 1/3rd, however, will arise along the serrated pathway, developed from the precursor lesion known as the sessile serrated adenoma (SSA). This is caused from an extensive methylation at the CpG island promoter site, which may demonstrate microsatellite instability. While controversy exits, it has been reported that SSAs are precursor lesions to micro-satellite unstable carcinomas; though limited data on the rate of progression currently exists[40]. In their pre-malignant state, these polyps show features between those of hyperplastic polyps and adenomas. On a molecular level, they have a high proportion of the BRAF mutation and DNA methylation. BRAF, a member of the RAF family of serine/threonine kinases, mediates cellular responses to growth signals, and BRAF mutations have been strongly associated with mis-match repair-deficient colorectal cancer[41]. Methylation and inactivation of the DNA repair genes MLH1 and MGMT (06 methylguanine-DNA methyltransferase) similar to that in hereditary non-polyposis colorectal cancer (HNPCC), are felt to be the critical steps that lead to this instability[42]. It has also previously been found that patients with micro-satellite unstable cancers demonstrate an increased serrated polyp to adenoma ratio compared to those with stable cancers. Therefore when encountering patients that have more serrated polyps than adenomas during colonoscopy, subsequent cancers in these patients may demonstrate MSI and should be considered for appropriate testing[43]. Risk factors for the development of sessile serrated adenomas include greater than 20 pack-year smoking history (OR = 7.31, 95%CI: 3.9-13.6), and, to a smaller extent, diabetes and obesity[44].

Unfortunately, there continues to be inconsistencies in the literature regarding the ultimate prognosis and malignant potential of both flat polyps and serrated adenomas. Even large series comparing flat lesions with polypoid have found that the size of the lesion confers much greater risk than the morphology for the development of malignancy. Furthermore, the incidence of high-grade dysplasia or cancer in flat neoplasms was found to be similar to that of polypoid neoplasms (5.4% vs 4.6%, P = 0.36) [45]. While still somewhat controversial, what seems increasingly clear is that while further information is required to determine the exact malignant risk of these lesions, there is evidence to suggest that they have a higher risk profile and should be followed accordingly.

Laterally spreading tumors

Another subset of high-risk lesions includes laterally spreading tumors (LSTs). These lesions have been increasingly described over the past 20 years and are characterized by their higher likelihood to spread laterally along the lumenal wall rather than vertically[46]. By definition, LSTs applies to lesions > 10 mm in diameter[47]. Okamoto initially described two clinical and histologic subtypes, which are identified as the granular-type (LST-G) and non-granular (LST-NG) [48]. Granular types appear endoscopically as multiple even or uneven nodules with the same color with its surrounding normal mucosa, while the non-granular type (also referred to as flat) appear smooth. These lesions may also be further stratified based on their morphological appearance as LST-G-H (homogenous) and LST-G-M (nodular mixed) type or LST-NG-F (flat elevated) and LST-NG-FD (pseudodepressed)[49].

These lesions have a much higher propensity for being missed via standard white light colonoscopy, as well as more advanced techniques such as narrow band imaging (NBI) and chromoendoscopy[50]. More importantly, LSTs have an increased rate of submucosal invasion. Rates of invasion, particularly for the LST-NG subtype are as high as 30%-40%[46],  whereas the granular subtype are significantly lower (about 5%-10%)[51]. While the risk of lymph node metastases is low for early invasion[52], the preferred management is still somewhat controversial, but mostly based on clinical and morphological appearance[53, 54]. What is clear, however, is that these lesions represent a high-risk group with a substantial rate of concomitant malignancy, and endoscopists need to have an acute awareness of their potential presence and follow-up on them accordingly.

POLYP DETECTION

There is little doubt that colonoscopy is a highly specific and sensitive test for the detection of colonic lesions, and several factors play a role in the adenoma detection rate (Table 1). However, differentiating early colon cancer from polyps can be more difficult. Factors that are associated with the presence of malignancy in a colonic polyp include villous architecture, increasing size, presence of multiple polyps and sessile lesions[55]. To further help in distinguishing benign from cancerous lesions, Kudo and colleagues in 1994 reported on differences in mucosal pit patterns of various colorectal polyps[56]. In this classification system, staining patterns that are often seen in hyperplastic polyps or normal mucosa differ from the unstructured surface architecture more commonly identified with malignancy. Pit patterns were classified into seven principal types: (1) normal round pit; (2) small round pit; (3) small asteroid pit; (4) large asteroid pit; (5) oval pit; (6) gyrus-like pit; and (7) non-pit. The authors found that there was a correlation between pit patterns and the histology of the cells in the gland. The authors further went on to categorize these seven principle types into 5 pit patterns: (1) normal round pit; (2) small and large asteroid pits; (3) small round pit; (4) oval pit; (5) gyrus-like pit; and (6) non-pit pattern. By using this schema, types I and II are non-neoplastic and III, IV, and V are neoplastic, with accuracy rates reported as high as 90%[57]. Chromoendoscopy and narrow band imaging (NBI) use these differences in pit pattern to help detect and differentiate polyps.

Chromoendoscopy

In chromoendoscopy, a dye such as indigo carmine can further enhance the surface structure of epithelial lesions with the aid of magnifying endoscopy[58]. Pit patterns become more recognizable, and outlining the borders of polyps is reported to be more accurate. Accuracy rates have been reported as high as 87%-100% and 76%-99.8% in diagnosing non-neoplastic and neoplastic polyps, respectively[59]. Furthermore, this technique has been shown to be beneficial for helping detect small lesions and decreasing the missed polyp rate, with diagnostic accuracies of 95% with magnification chromoendoscopy for lesions < 5 mm compared to 76% with traditional colonoscopy[60, 61]. A recent update of the Cochrane review consisting of 5 studies compared chromoendoscopy versus conventional endoscopy for detection of polyps, and showed that chromoendoscopy is more apt to identify patients with at least one neoplastic lesion (OR = 1.67, 95%CI: 1.29-2.15), as well as those with ≥ 3 neoplastic lesions (OR = 2.55, 95%CI: 1.49-4.36) over “white” light endoscopy[62]. Although still not widely used, especially in the United States, chromoendoscopy has also been cited to reduce the time, cost and risk with biopsy/polypectomy, once the initial learning curve associated with dye application is complete.

NARROW BAND IMAGING

Narrow band imaging (NBI) is an imaging technique that also relies on better definition of capillary pattern to improve the contrast between adenomas and surrounding normal mucosa. Adenomas, like malignancy, have a characteristic angiogenesis that can be detected using various wavelengths of light that variably penetrate the colon mucosa[63]. The theory behind it’s efficacy lies in its ability to contrast the “normal” mucosa from that of adenomatous tissue to a greater degree than standard white light colonoscopy by selecting out specific wavelengths through optical filters that “narrow” the bandwidth of light. Developed by Gono and associates (and originally described on the vascular pattern and adjacent mucosa of the underside of the human tongue), it uses the reflected light to visualize the superficial structure and enhance the vasculature within the mucosal layers[63]. Unlike chromoendoscopy, which relies on sprays and specialized equipment, NBI is readily available on many colonoscopy systems and does not require additional imaging. The data supporting its use, however, remains somewhat conflicting. In a pilot study by Machida and associates, NBI had a 93.4% diagnostic accuracy, equivalent to chromoendoscopy with magnification, and higher than that of conventional colonoscopy[64]. In one randomized trial during screening colonoscopies, patients randomized to white light (n = 108) and NBI (n = 103) had adenoma detection rates of 58.3 and 57.3 (P = 0.88), respectively. However, when the authors further evaluated only flat adenomas, a lesion believed to be best defined by NBI, the detection rates were 9.3% for traditional colonoscopy and 21.4% for NBI (P = 0.019)[65]. Other randomized data including 1,256 patients comparing NBI technology to white light with associated high definition video found no difference in overall adenoma detection rates (33% vs 34%), total number of lesions (200 vs 216), or any other subgroups of adenomas to include flat lesions[66]. In this study, only hyperplastic polyps were found more commonly in NBI. Several other authors have found NBI did not improve the colorectal neoplasm miss rate compared to traditional methods[67], or even those of small and flat adenomas with the use of high-definition colonoscope[68]. A recent Cochrane review identified 11 randomized trials with 3,673 patients comparing NBI to standard white light endoscopy for the detection of colorectal polyps. The authors found similar rates of overall polyp detection (6 trials, n = 2832, RR = 0.97, 95%CI: 0.91-1.04), and adenomas (8 trials, n = 3673, RR = 0.94, 95%CI: 0.87-1.02), even when stratifying by the number of patients with at least one lesion by size [< 5 mm: RR = 0.95, 95%CI: 0.84-1.08, I2 = 56%; 6 to 9 mm: RR = 1.06, 95%CI: 0.81-1.39, I2 = 0%; ≥ 10 mm: RR = 1.06, 95%CI: 0.77 to 1.45, I2 = 0%][69].

On the contrary, there are studies that do report improvements in distinguishing neoplastic from non-neoplastic lesions using NBI, with accuracy rates higher than that of colonoscopy and equivalent to chromoendoscopy (80-82% low magnification NBI; 85% low magnification chromoendoscopy; 87-90% high magnification NBI; 82%-92% high magnification chromoendoscopy; standard colonoscopy (67%-68%)[70]. Other authors have found sensitivity of 90%-96% and specificity of 85%-89% in differentiation of neoplastic versus non-neoplastic lesions, comparable to that of chromoendoscopy. Furthermore, accuracy rates were even higher with the addition of magnifying endoscopy, up to 94% for neoplastic and 89% for non-neoplastic lesions[71, 72]. Similar to chromoendoscopy, however, the ultimate role this will have relies on the long-term data, ability to lower costs, and proper training of endoscopists prior to incorporation into everyday and widespread use.

Endoscopic mucosal resection and endoscopic submucosal dissection

Endoscopic mucosal resection

Endoscopic mucosal resection (EMR) was first described in 1990 by Inoue and Endo in Japan[73], and subsequently followed by Soehendra and colleagues in Hamburg, Germany in 1997[74]. In the esophagus and stomach, as well as the colon, EMR allows removal of superficial tumors of the gastrointestinal tract. Unlike polypectomy that removes the tumor at the base of the mucosa, the plane of resection during EMR occurs in the middle or deep submucosal layer. Drawbacks of piecemeal excision include difficulty with proper staging, histological diagnosis, and definitive evaluation of the margins[46,75]. Furthermore, unlike the stomach, the colonic wall is much thinner and haustrated, leading to a technically more difficult procedure. Indications for EMR currently include adenomas or small, well-differentiated carcinomas confined to the mucosa or with minimal invasion into the submucosa, those more than 1/3rd of the lumenal diameter, or flat/depressed polyps. In essence, EMR enables select lesions to be removed endoscopically that would potentially require colectomy[76]. It is important that these early carcinomas do not have lymphovascular invasion, due to the increased risk of lymph node metastases. As this technique is currently performed more commonly in Japan, the Japanese Society for Cancer of the Colon and Rectum’s current criteria for curative endoscopic resection are: submucosal invasion of less than 1000 μm, moderate or well-differentiated lesion characteristics, and the absence of vascular invasion[77]. Moss and colleagues have also identified risk factors for submucosal invasion and failure of successful EMR in a prospective, multi-center cohort of 479 patients and 514 lesions[78]. In their collective experience, Paris classification 0-IIa+c morphology, nongranular surface, and Kudo pit pattern type V were all risk factors for invasion, with even higher risks (up to 55.5%) when multiple factors were present. EMR was attempted in 464 patients, being successful in 414 (89%), with a prior EMR attempt by the referring endoscopist (OR = 3.75; 95%CI: 1.77-7.94), difficult position (OR = 2.17; 95%CI: 1.14-4.12) and ileocecal valve location (OR = 3.38; 95%CI: 1.20-9.52) all predictors of initial failure.

Local recurrence has been reported in 6.9%-13.4% of cases of EMR, with higher rates reported following piecemeal excision, invasive pathology, and for lesions >2 m (rates up to 39%)[79]. Median times for recurrence are typically within the first 6 mo, signifying the importance of follow-up endoscopic evaluation between 3 mo and one year[80]. In patients with larger polyps or those with dysplasia or cancer, it is recommended that they undergo more high intensity surveillance[81, 82]. Other reported risk factors for recurrence include a granulous appearance of the lesion and distal rectal lesions. Incomplete (R1) resections and those with deep positive margins should be considered for surgery.

Outcomes for EMR are, in general, very good as most patients are highly selected. When performed by experts, less than 3% of lesions are referred for surgical resection (due to inadequate removal), 44%-60% are performed en bloc, and the remaining lesions undergo successful piecemeal removal[83]. In sample series, complications involve procedural (10%-13%) and late (0%-1%) bleeding, post-polypectomy syndrome (2%-3%) and perforations (1%-2%)[84]. In attempt to identify high risk polyps that contain cancer prior to EMR, several authors have shown malignancy rates are higher with sessile polyps and those > 3 cm[83, 84]. Although these factors are not absolute contraindications to EMR, it is typically more difficult to remove tumors larger than 2cm by en bloc resection using EMR, with reported rates of about 30%. The decision to perform EMR should be made on an individual basis[85-87].

Endoscopic submucosal dissection

Endoscopic submucosal dissection (ESD) is primarily used to help with resecting larger tumors and aid in achieving higher rates of en-bloc resection of superficial tumors in the gastrointestinal tract than EMR. While EMR is the current standard in most centers outside of Asia, ESD is a technique that should, in general, be reserved for highly selected lesions by specialized endoscopists skilled and experienced in this technique Although still primarily performed in select centers and lacking widespread use, the goals of ESD remain: (1) treating mucosal cancer; (2) achieving an R0 resection; (3) meeting quality standards; and (4) ensuring that procedures are performed by endoscopists trained in this technique and under institutional review board approval[88]. As a general guideline, ESD is more commonly indicated when a snare is unlikely to enable a successful en bloc resection with EMR. ESD is also indicated when tumors are diagnosed as carcinomas with intramucosal to shallow submucosal invasion, as well as lesions with submucosal fibrosis that cannot be removed by EMR, even if less than 20mm in size. Others have proposed that this technique is suitable for all large polyps, early colorectal cancer, and those lesions that cannot be accessed transanally in patients who wish to avoid major resection.

Similar to other new technology, both EMR and ESD have learning curves that play a large role in determining outcomes. Previous reports out of Asia, where experience tends to be much greater, have demonstrated proficiency for larger lesions occurs at about 80 cases, with generalized avoidance of major complications such as perforation at about 30-40 procedures[89, 90]. Yet, the learning curve of ESD and its outcome comparison to EMR in centers where endoscopists are not as familiar or experienced is less defined to date. Probst and colleagues evaluated their learning curve in a European study of 82 rectosigmoid lesions, with successful resection using ESD techniques in 76 (93%)[91]. Over the 7-year study period, the authors divided up their experience into three separate phases (1-25, 26-50 and 51-76). During this time, both the rates of en-bloc resection (60%, 88% and 96%, respectively) and R0 resection (80%, 86% and 88%) increased, while procedure times significantly decreased (200 min, 193 min  and 136 min ).

Using different techniques, other authors have reported successful en-bloc resection occurs in up to 85%-89% of cases and piece-meal resection is possible in the remaining 10%-15%[92-96]. Clear lateral and deep margins (i.e, complete resections) have been reported in up to 79%-86% of cases[97, 98]. As previously stated, because it is difficult to perform en-bloc resection by EMR for lesions larger than 20 mm, ESD may be more suitable for these lesions. The ability to predict depth of invasion in an attempt to decide whether to pursue EMR, ESD or formal resection remains somewhat difficult. Similar to EMR studies, predictors of submucosal versus mucosal invasion include poor-differentiation and the absence of background adenoma[83, 84].

Briefly the technique of ESD involves an initial bowel preparation to remove residual feces. An endoscope with a single channel is used along with a high-frequency electrosurgical generator. After identification of a lesion, one of several types of solutions (including a mixture of 1% hyaluronic acid solution and 10% glycerin solution) is injected around the lesions to elevate the submucosa[99]. Specialized knives in various shapes and sizes help to perform the dissection and resection. The border of the tumor is initially marked by indigo carmine dye and with approximately 1 cm margins. Following a mucosal incision, and depending on the physician preference, a partial or circumferential incision is made along with injection of hyaluronic acid solution into the submucosa, and the dissection is carried down to the deep submucosa. This process is continued around the tumor until the entire lesion is resected en bloc, when possible.

Perforation using ESD occurs in 1.4%-10.4% of cases, with the majority of series reporting rates < 2%[100]. These rates are classically higher than reported with EMR and are most likely due to the depth of dissection, and in certain cases lesions that are associated with a significant amount of fibrosis[101]. When small perforations occur, endoscopic clips have been utilized to close the site when feasible[102]. In more severe cases or those that cannot be closed endoscopically, more definitive procedures should be performed either by laparoscopy or laparotomy. Cases of delayed perforation occur in < 1% of cases, and are thought to be a result of thermal injury[103]. Postoperative hemorrhage rates are reported between 0%-12%, comparable to that with EMR, and the majority are self-limiting[96]. Another not infrequent complication is the inability to complete the procedure secondary to patient restlessness from abdominal distension and pain (12%-32%), requiring additional conscious sedation or even general anesthesia. Additionally, the use of carbon dioxide has been shown to significantly reduce this pain and bloating when deep sedation compared to traditional air insufflation[104]. Other more rare complications include obstruction, fever, and pain[105]. Most importantly, residual disease has been reported in 2%-3% with ESD[106]. In one of the few series comparing ESD with EMR, 145 colorectal tumors were treated by ESD and another 228 treated by EMR. ESD was associated with a longer procedure time (108 min vs 29 min, P < 0.0001), higher en bloc resection rate (84% vs 33%, P < 0.0001) and larger resected specimen size (37 mm vs 28 mm; P = 0.0006) [86]. There were three (2%) recurrences in the ESD group and 33 (14%) in the EMR group requiring additional EMR (P < 0.0001). Complication rates were similar (perforation 6.2% ESD vs 1.3% EMR; delayed bleeding 1.4% ESD vs 3.1% EMR; P = NS). Although both of these techniques are currently only offered in select centers, emerging literature and advances in technology may provide the impetus for more widespread training and utilization.

Combined laparoscopic-endoscopic resection/ combined endoscopic-laparoscopic surgery

It is important to note that most lesions can (and should) be approached through traditional techniques. However, for select more advanced lesions, other methods are available. Combined laparoscopic-endoscopic resection or combined endoscopic-laparoscopic surgery offers another approach for the removal of these advanced lesions that are not amenable to traditional endoscopic techniques, and would normally go on to formal resection. Lesions that are identified as being larger or more difficult to remove in the endoscopy suite are marked, and the patient is taken for a procedure under general anesthesia. In the operating room, the subcutaneous layer under the polyp is injected to lift the polyp. After laparoscopic ports are placed, the bowel is manipulated from the outside to expose the base of the lesion, and endoscopic polypectomy is performed. This enables direct evaluation for any full thickness injury, as well as the ability to imbricate or close the bowel wall using full thickness sutures should the need arise. Additionally, a sleeve resection can be performed that removes the lesion along with a full-thickness section of the surrounding wall (i.e., in cecal lesions). A leak test can also be performed by submersion of the staple/suture line under water along with CO2 or air insufflation. Any concerns regarding the applicability of the lesion for this procedure are alleviated by immediate conversion to a standard laparoscopic-assisted oncological resection[107].

Technical success rates have consistently been reported in 77%-97%, with the remaining requiring conversion to resection[108, 109]. Common reasons for an inability to perform this procedure include difficult lesion location, poor visualization (which has been aided by CO2-insufflation), and concerns for malignancy. Post-operative complications have been generally < 10%, with the majority being minor wound infections, bleeding, and ileus. Major complications are rare, with many reports citing a 0%-3% incidence. Recurrence rates are also low, reported in 10%-15% and typically are benign that may be approached via similar CLER, standard endoscopy or formal resection[107-109]. Final pathology ultimately will dictate the need for any subsequent segmental resection, and patients should be counseled about this ahead of time. Novel approaches for large and advanced polyps are available to surgeons that may obviate the need for formal resection. Although technical expertise and experience is required, physicians caring for these patients should be familiar with these alternative procedures.

CONCLUSION

Our goal remains to identify and intervene on lesions at the polyp stage, prior to invasion. While colonoscopy is the most effective screening tool to detect pre-cancerous polyps and colon cancer, we must focus on the quality indicators such as withdrawal time and adenoma detection rate to ultimately improve our outcomes. Advances such as NBI, chromoendoscopy, endoscopic mucosal resection, endoscopic submucosal dissection, and combined laparoscopic-endoscopic resection are tools that may improve the management of benign and early malignant polyps, and physicians performing endoscopy should be well-versed in their applicability and efficacy.

REFERENCES

1 Morgenthal CB, Richards WO, Dunkin BJ, Forde KA, Vitale G, Lin E. The role of the surgeon in the evolution of flexible endoscopy. Surg Endosc 2007; 21: 838-853 [PMID: 17180263 DOI: 10.1007/s00464-006-9109-4]

2 Mandel JS, Bond JH, Church TR, Snover DC, Bradley GM, Schuman LM, Ederer F. Reducing mortality from colorectal cancer by screening for fecal occult blood. Minnesota Colon Cancer Control Study. N Engl J Med 1993; 328: 1365-1371 [PMID: 8474513 DOI: 10.1056/NEJM199305133281901]

3 Hardcastle JD, Chamberlain JO, Robinson MH, Moss SM, Amar SS, Balfour TW, James PD, Mangham CM. Randomised controlled trial of faecal-occult-blood screening for colorectal cancer. Lancet 1996; 348: 1472-1477 [PMID: 8942775 DOI: 10.1016/S0140-6736(96)03386-7]

4 Selby JV, Friedman GD, Quesenberry CP, Weiss NS. A case-control study of screening sigmoidoscopy and mortality from colorectal cancer. N Engl J Med 1992; 326: 653-657 [PMID: 1736103 DOI: 10.1056/NEJM199203053261001]

5 Newcomb PA, Norfleet RG, Storer BE, Surawicz TS, Marcus PM. Screening sigmoidoscopy and colorectal cancer mortality. J Natl Cancer Inst 1992; 84: 1572-1575 [PMID: 1404450 DOI: 10.1093/jnci/84.20.1572]

6 Lieberman DA, Weiss DG, Bond JH, Ahnen DJ, Garewal H, Chejfec G. Use of colonoscopy to screen asymptomatic adults for colorectal cancer. Veterans Affairs Cooperative Study Group 380. N Engl J Med 2000; 343: 162-168 [PMID: 10900274 DOI: 10.1056/NEJM200007203430301]

7 Imperiale TF, Wagner DR, Lin CY, Larkin GN, Rogge JD, Ransohoff DF. Risk of advanced proximal neoplasms in asymptomatic adults according to the distal colorectal findings. N Engl J Med 2000; 343: 169-174 [PMID: 10900275 DOI: 10.1056/NEJM200007203430302]

8 Harewood GC, Lieberman DA. Colonoscopy practice patterns since introduction of medicare coverage for average-risk screening. Clin Gastroenterol Hepatol 2004; 2: 72-77 [PMID: 15017635 DOI: 10.1016/S1542-3565(03)00294-5]

9 Rex DK, Cutler CS, Lemmel GT, Rahmani EY, Clark DW, Helper DJ, Lehman GA, Mark DG. Colonoscopic miss rates of adenomas determined by back-to-back colonoscopies. Gastroenterology 1997; 112: 24-28 [PMID: 8978338 DOI: 10.1016/S0016-5085(97)70214-2]

10 van Rijn JC, Reitsma JB, Stoker J, Bossuyt PM, van Deventer SJ, Dekker E. Polyp miss rate determined by tandem colonoscopy: a systematic review. Am J Gastroenterol 2006; 101: 343-350 [PMID: 16454841 DOI: 10.1111/j.1572-0241.2006.00390.x]

11 Heresbach D, Barrioz T, Lapalus MG, Coumaros D, Bauret P, Potier P, Sautereau D, Boustière C, Grimaud JC, Barthélémy C, Sée J, Serraj I, D'Halluin PN, Branger B, Ponchon T. Miss rate for colorectal neoplastic polyps: a prospective multicenter study of back-to-back video colonoscopies. Endoscopy 2008; 40: 284-290 [PMID: 18389446 DOI: 10.1055/s-2007-995618]

12 Lebwohl B, Kastrinos F, Glick M, Rosenbaum AJ, Wang T, Neugut AI. The impact of suboptimal bowel preparation on adenoma miss rates and the factors associated with early repeat colonoscopy. Gastrointest Endosc 2011; 73: 1207-1214 [PMID: 21481857 DOI: 10.1016/j.gie.2011.01.051.]

13 Rex DK. Colonoscopic withdrawal technique is associated with adenoma miss rates. Gastrointest Endosc 2000; 51: 33-36 [PMID: 10625792 DOI: 10.1016/S0016-5107(00)70383-X]

14 Sawhney MS, Cury MS, Neeman N, Ngo LH, Lewis JM, Chuttani R, Pleskow DK, Aronson MD. Effect of institution-wide policy of colonoscopy withdrawal time & gt; or = 7 minutes on polyp detection. Gastroenterology 2008; 135: 1892-1898 [PMID: 18835390 DOI: 10.1053/j.gastro.2008.08.024]

15 Simmons DT, Harewood GC, Baron TH, Petersen BT, Wang KK, Boyd-Enders F, Ott BJ. Impact of endoscopist withdrawal speed on polyp yield: implications for optimal colonoscopy withdrawal time. Aliment Pharmacol Ther 2006; 24: 965-971 [PMID: 16948808 DOI: 10.1111/j.1365-2036.2006.03080.x]

16 Sanchez W, Harewood GC, Petersen BT. Evaluation of polyp detection in relation to procedure time of screening or surveillance colonoscopy. Am J Gastroenterol 2004; 99: 1941-1945 [PMID: 15447753 DOI: 10.1111/j.1572-0241.2004.40569]

17 Barclay RL, Vicari JJ, Doughty AS, Johanson JF, Greenlaw RL. Colonoscopic withdrawal times and adenoma detection during screening colonoscopy. N Engl J Med 2006; 355: 2533-2541 [PMID: 17167136 DOI: 10.1056/NEJMoa055498]

18 Overholt BF, Brooks-Belli L, Grace M, Rankin K, Harrell R, Turyk M, Rosenberg FB, Barish RW, Gilinsky NH. Withdrawal times and associated factors in colonoscopy: a quality assurance multicenter assessment. J Clin Gastroenterol 2010; 44: e80-e86 [PMID: 19881361 DOI: 10.1097/MCG.0b013e3181bf9b02]

19 Benson ME, Reichelderfer M, Said A, Gaumnitz EA, Pfau PR. Variation in colonoscopic technique and adenoma detection rates at an academic gastroenterology unit. Dig Dis Sci 2010; 55: 166-171 [PMID: 19156519 DOI: 10.1007/s10620-008-0703-2]

20 Gellad ZF, Weiss DG, Ahnen DJ, Lieberman DA, Jackson GL, Provenzale D. Colonoscopy withdrawal time and risk of neoplasia at 5 years: results from VA Cooperative Studies Program 380. Am J Gastroenterol 2010; 105: 1746-1752 [PMID: 20234348 DOI: 10.1038/ajg.2010.107]

21 Lin OS, Kozarek RA, Arai A, Gluck M, Jiranek GC, Kowdley KV, McCormick SE, Schembre DB, Soon MS, Dominitz JA. The effect of periodic monitoring and feedback on screening colonoscopy withdrawal times, polyp detection rates, and patient satisfaction scores. Gastrointest Endosc 2010; 71: 1253-1259 [PMID: 20598251 DOI: 10.1016/j.gie.2010.01.017]

22 Taber A, Romagnuolo J. Effect of simply recording colonoscopy withdrawal time on polyp and adenoma detection rates. Gastrointest Endosc 2010; 71: 782-786 [PMID: 20363418 DOI: 10.1016/j.gie.2009.12.008]

23 Imperiale TF, Glowinski EA, Juliar BE, Azzouz F, Ransohoff DF. Variation in polyp detection rates at screening colonoscopy. Gastrointest Endosc 2009; 69: 1288-1295 [PMID: 19481649 DOI: 10.1016/j.gie.2007.11.043]

24 Warneke J, Petrelli N, Herrera L, Nava H. Accuracy of colonoscopy for the detection of colorectal polyps. Dis Colon Rectum 1992; 35: 981-985 [PMID: 1395987 DOI: 10.1007/BF02253502]

25 Sanaka MR, Shah N, Mullen KD, Ferguson DR, Thomas C, McCullough AJ. Afternoon colonoscopies have higher failure rates than morning colonoscopies. Am J Gastroenterol 2006; 101: 2726-2730 [PMID: 17227519 DOI: 10.1111/j.1572-0241.2006.00887.x]

26 Wells CD, Heigh RI, Sharma VK, Crowell MD, Gurudu SR, Leighton JA, Mattek N, Fleischer DE. Comparison of morning versus afternoon cecal intubation rates. BMC Gastroenterol 2007; 7: 19 [PMID: 17559669 DOI: 10.1186/1471-230X-7-19]

27 Sanaka MR, Deepinder F, Thota PN, Lopez R, Burke CA. Adenomas are detected more often in morning than in afternoon colonoscopy. Am J Gastroenterol 2009; 104: 1659-164; quiz 1665 [PMID: 19491841 DOI: 10.1038/ajg.2009.249]

28 Gurudu SR, Ratuapli SK, Leighton JA, Heigh RI, Crowell MD. Adenoma detection rate is not influenced by the timing of colonoscopy when performed in half-day blocks. Am J Gastroenterol 2011; 106: 1466-1471 [PMID: 21502998 DOI: 10.1038/ajg.2011.125.]

29 Lee A, Iskander JM, Gupta N, Borg BB, Zuckerman G, Banerjee B, Gyawali CP. Queue position in the endoscopic schedule impacts effectiveness of colonoscopy. Am J Gastroenterol 2011; 106: 1457-1465 [PMID: 21448145 DOI: 10.1038/ajg.2011.87]

30 Rostom A, Ross ED, Dubé C, Rutter MD, Lee T, Valori R, Bridges RJ, Pontifex D, Webbink V, Rees C, Brown C, Whetter DH, Kelsey SG, Hilsden RJ. Development and validation of a nurse-assessed patient comfort score for colonoscopy. Gastrointest Endosc 2013; 77: 255-261 [PMID: 23317691 DOI: 10.1016/j.gie.2012.10.003]

31 Kaltenbach T, Leung C, Wu K, Yan K, Friedland S, Soetikno R. Use of the colonoscope training model with the colonoscope 3D imaging probe improved trainee colonoscopy performance: a pilot study. Dig Dis Sci 2011; 56: 1496-1502 [PMID: 21409379 DOI: 10.1007/s10620-011-1614-1]

32 Anderson JC. Risk factors and diagnosis of flat adenomas of the colon. Expert Rev Gastroenterol Hepatol 2011; 5: 25-32 [PMID: 21309669 DOI: 10.1586/egh.10.86]

33 Kudo S. Endoscopic mucosal resection of flat and depressed types of early colorectal cancer. Endoscopy 1993; 25: 455-461 [PMID: 8261988 DOI: 10.1055/s-2007-1010367]

34 The Paris endoscopic classification of superficial neoplastic lesions: esophagus, stomach, and colon: November 30 to December 1, 2002. Gastrointest Endosc 2003; 58: S3-43 [PMID: 14652541 DOI: 10.1016/S0016-5107(03)02159-X]

35 Speake D, Biyani D, Frizelle FA, Watson AJ. Flat adenomas. ANZ J Surg 2007; 77: 4-8 [PMID: 17295810 DOI: 10.1111/j.1445-2197.2006.03847.x]

36 Goldstein NS. Serrated pathway and APC (conventional)-type colorectal polyps: molecular-morphologic correlations, genetic pathways, and implications for classification. Am J Clin Pathol 2006; 125: 146-153 [PMID: 16483003 DOI: 10.1309/87BD0C6UCGUG236J]

37 Noffsinger AE, Hart J. Serrated adenoma: a distinct form of non-polypoid colorectal neoplasia? Gastrointest Endosc Clin N Am 2010; 20: 543-563 [PMID: 20656251 DOI: 10.1016/j.giec.2010.03.012]

38 Muto T, Bussey HJ, Morson BC. The evolution of cancer of the colon and rectum. Cancer 1975; 36: 2251-2270 [PMID: 1203876 DOI: 10.1002/cncr.2820360944]

39 Vogelstein B, Fearon ER, Hamilton SR, Kern SE, Preisinger AC, Leppert M, Nakamura Y, White R, Smits AM, Bos JL. Genetic alterations during colorectal-tumor development. N Engl J Med 1988; 319: 525-532 [PMID: 2841597 DOI: 10.1056/NEJM198809013190901]

40 Snover DC. Update on the serrated pathway to colorectal carcinoma. Hum Pathol 2011; 42: 1-10 [PMID: 20869746 DOI: 10.1016/j.humpath.2010.06.002]

41 Kambara T, Simms LA, Whitehall VL, Spring KJ, Wynter CV, Walsh MD, Barker MA, Arnold S, McGivern A, Matsubara N, Tanaka N, Higuchi T, Young J, Jass JR, Leggett BA. BRAF mutation is associated with DNA methylation in serrated polyps and cancers of the colorectum. Gut 2004; 53: 1137-1144 [PMID: 15247181 DOI: 10.1136/gut.2003.037671]

42 Jass JR. Serrated adenoma of the colorectum and the DNA-methylator phenotype. Nat Clin Pract Oncol 2005; 2: 398-405 [PMID: 16130936 DOI: 10.1038/ncponc0248]

43 Messick CA, Church J, Casey G, Kalady MF. Identification of the methylator (serrated) colorectal cancer phenotype through precursor serrated polyps. Dis Colon Rectum 2009; 52: 1535-1541 [PMID: 19690479 DOI: 10.1007/DCR.0b013e3181afbe05]

44 Anderson JC, Rangasamy P, Rustagi T, Myers M, Sanders M, Vaziri H, Wu G, Birk JW, Protiva P. Risk factors for sessile serrated adenomas. J Clin Gastroenterol 2011; 45: 694-699 [PMID: 21325950 DOI: 10.1097/MCG.0b013e318207f3cf]

45 Park DH, Kim HS, Kim WH, Kim TI, Kim YH, Park DI, Kim HJ, Yang SK, Byeon JS, Lee MS, Chung IK, Jung SA, Jeen YT, Choi JH, Choi H, Han DS. Clinicopathologic characteristics and malignant potential of colorectal flat neoplasia compared with that of polypoid neoplasia. Dis Colon Rectum 2008; 51: 43-9; discussion 49 [PMID: 18034359]

46 Hurlstone DP, Sanders DS, Cross SS, Adam I, Shorthouse AJ, Brown S, Drew K, Lobo AJ. Colonoscopic resection of lateral spreading tumours: a prospective analysis of endoscopic mucosal resection. Gut 2004; 53: 1334-1339 [PMID: 15306595 DOI: 10.1136/gut.2003.036913]

47 Kudo S, Kashida H, Nakajima T, Tamura S, Nakajo K. Endoscopic diagnosis and treatment of early colorectal cancer. World J Surg 1997; 21: 694-701 [PMID: 9276699 DOI: 10.1007/s002689900293]

48 Okamoto T, Tanaka S, Haruma K, Hiraga Y, Kunihiro M, Goishi H, Tanimoto T, Sumii M, Yoshihara M, Sumii K, Kajiyama G, Shimamoto F. [Clinicopathologic evaluation on colorectal laterally spreading tumor (LST)]. Nihon Shokakibyo Gakkai Zasshi 1996; 93: 83-89 [PMID: 8865747]

49 Nishiyama H, Isomoto H, Yamaguchi N, Ishii H, Fukuda E, Machida H, Nakamura T, Ohnita K, Shikuwa S, Kohno S, Nakao K. Endoscopic submucosal dissection for laterally spreading tumours of the colorectum in 200 consecutive cases. Surg Endosc 2010; 24: 2881-2887 [PMID: 20419319 DOI: 10.1007/s00464-010-1071-5]

50 Tamai N, Saito Y, Sakamoto T, Nakajima T, Matsuda T, Vikneswaran N, Tajiri H. Visualization of laterally spreading colorectal tumors by using image-enhanced endoscopy. Gastroenterol Res Pract 2012; 2012: 638391 [PMID: 22461788 DOI: 10.1155/2012/638391]

51 Kim BC, Chang HJ, Han KS, Sohn DK, Hong CW, Park JW, Park SC, Choi HS, Oh JH. Clinicopathological differences of laterally spreading tumors of the colorectum according to gross appearance. Endoscopy 2011; 43: 100-107 [PMID: 21165823 DOI: 10.1055/s-0030-1256027.]

52 Kudo S, Kashida H, Tamura T, Kogure E, Imai Y, Yamano H, Hart AR. Colonoscopic diagnosis and management of nonpolypoid early colorectal cancer. World J Surg 2000; 24: 1081-1090 [PMID: 11036286 DOI: [10.1007/s002680010154]

53 Lambert R, Tanaka S. Laterally spreading tumors in the colon and rectum. Eur J Gastroenterol Hepatol 2012; 24: 1123-1134 [PMID: 22732357 DOI: 10.1097/MEG.0b013e328355e2d9]

54 Repici A, Hassan C, Pagano N, Rando G, Romeo F, Spaggiari P, Roncalli M, Ferrara E, Malesci A. High efficacy of endoscopic submucosal dissection for rectal laterally spreading tumors larger than 3 cm. Gastrointest Endosc 2013; 77: 96-101 [PMID: 23261098 DOI: 10.1016/j.gie.2012.08.036]

55 Cappell MS, Friedel D. The role of sigmoidoscopy and colonoscopy in the diagnosis and management of lower gastrointestinal disorders: endoscopic findings, therapy, and complications. Med Clin North Am 2002; 86: 1253-1288 [PMID: 12510454 DOI: 10.1016/S0025-7125(02)00077-9]

56 Kudo S, Hirota S, Nakajima T, Hosobe S, Kusaka H, Kobayashi T, Himori M, Yagyuu A. Colorectal tumours and pit pattern. J Clin Pathol 1994; 47: 880-885 [PMID: 7962600 DOI: 10.1136/jcp.47.10.880]

57 Su MY, Ho YP, Chen PC, Chiu CT, Wu CS, Hsu CM, Tung SY. Magnifying endoscopy with indigo carmine contrast for differential diagnosis of neoplastic and nonneoplastic colonic polyps. Dig Dis Sci 2004; 49: 1123-1127 [PMID: 15387332 DOI: 0.1023/B: DDAS.0000037798.55845.f7]

58 Fujii T, Hasegawa RT, Saitoh Y, Fleischer D, Saito Y, Sano Y, Kato S. Chromoscopy during colonoscopy. Endoscopy 2001; 33: 1036-1041 [PMID: 11764766]

59 Wada Y, Kashida H, Kudo SE, Misawa M, Ikehara N, Hamatani S. Diagnostic accuracy of pit pattern and vascular pattern analyses in colorectal lesions. Dig Endosc 2010; 22: 192-199 [PMID: 20642608 DOI: 10.1111/j.1443-1661.2010.00983.x]

60 Lapalus MG, Helbert T, Napoleon B, Rey JF, Houcke P, Ponchon T. Does chromoendoscopy with structure enhancement improve the colonoscopic adenoma detection rate? Endoscopy 2006; 38: 444-448 [PMID: 16767577 DOI: 0.1055/s-2006-925265]

61 Hurlstone DP, Cross SS, Slater R, Sanders DS, Brown S. Detecting diminutive colorectal lesions at colonoscopy: a randomised controlled trial of pan-colonic versus targeted chromoscopy. Gut 2004; 53: 376-380 [PMID: 14960519 DOI: 10.1136/gut.2003.029868]

62 Brown SR, Baraza W. Chromoscopy versus conventional endoscopy for the detection of polyps in the colon and rectum. Cochrane Database Syst Rev 2010; CD006439 [PMID: 20927746 DOI: 10.1002/14651858.CD006439.pub3]

63 Gono K, Obi T, Yamaguchi M, Ohyama N, Machida H, Sano Y, Yoshida S, Hamamoto Y, Endo T. Appearance of enhanced tissue features in narrow-band endoscopic imaging. J Biomed Opt 2004; 9: 568-577 [PMID: 15189095 DOI: 10.1117/1.1695563]

64 Machida H, Sano Y, Hamamoto Y, Muto M, Kozu T, Tajiri H, Yoshida S. Narrow-band imaging in the diagnosis of colorectal mucosal lesions: a pilot study. Endoscopy 2004; 36: 1094-1098 [PMID: 15578301 DOI: 10.1055/s-2004-826040]

65 Paggi S, Radaelli F, Amato A, Meucci G, Mandelli G, Imperiali G, Spinzi G, Terreni N, Lenoci N, Terruzzi V. The impact of narrow band imaging in screening colonoscopy: a randomized controlled trial. Clin Gastroenterol Hepatol 2009; 7: 1049-1054 [PMID: 19577008 DOI: 10.1016/j.cgh.2009.06.028]

66 Adler A, Aschenbeck J, Yenerim T, Mayr M, Aminalai A, Drossel R, Schröder A, Scheel M, Wiedenmann B, Rösch T. Narrow-band versus white-light high definition television endoscopic imaging for screening colonoscopy: a prospective randomized trial. Gastroenterology 2009; 136: 410-6.e1; quiz 715 [PMID: 19014944 DOI: 10.1053/j.gastro.2008.10.022]

67 Kaltenbach T, Friedland S, Soetikno R. A randomised tandem colonoscopy trial of narrow band imaging versus white light examination to compare neoplasia miss rates. Gut 2008; 57: 1406-1412 [PMID: 18523025 DOI: 10.1136/gut.2007.137984]

68 Rex DK, Helbig CC. High yields of small and flat adenomas with high-definition colonoscopes using either white light or narrow band imaging. Gastroenterology 2007; 133: 42-47 [PMID: 17631129 DOI: 10.1053/j.gastro.2007.04.029]

69 Nagorni A, Bjelakovic G, Petrovic B. Narrow band imaging versus conventional white light colonoscopy for the detection of colorectal polyps. Cochrane Database Syst Rev 2012; 1: CD008361 [PMID: 22258983 DOI: 10.1002/14651858.CD008361.pub2]

70 Chiu HM, Chang CY, Chen CC, Lee YC, Wu MS, Lin JT, Shun CT, Wang HP. A prospective comparative study of narrow-band imaging, chromoendoscopy, and conventional colonoscopy in the diagnosis of colorectal neoplasia. Gut 2007; 56: 373-379 [PMID: 17005766 DOI: 10.1136/gut.2006.099614]

71 Tischendorf JJ, Wasmuth HE, Koch A, Hecker H, Trautwein C, Winograd R. Value of magnifying chromoendoscopy and narrow band imaging (NBI) in classifying colorectal polyps: a prospective controlled study. Endoscopy 2007; 39: 1092-1096 [PMID: 18072061 DOI: 10.1055/s-2007-966781]

72 Su MY, Hsu CM, Ho YP, Chen PC, Lin CJ, Chiu CT. Comparative study of conventional colonoscopy, chromoendoscopy, and narrow-band imaging systems in differential diagnosis of neoplastic and nonneoplastic colonic polyps. Am J Gastroenterol 2006; 101: 2711-2716 [PMID: 17227517 DOI: 10.1111/j.1572-0241.2006.00932.x]

73 Inoue H, Endo M. Endoscopic esophageal mucosal resection using a transparent tube. Surg Endosc 1990; 4: 198-201 [PMID: 2291159 DOI: 10.1007/BF00316791]

74 Soehendra N, Binmoeller KF, Bohnacker S, Seitz U, Brand B, Thonke F, Gurakuqi G. Endoscopic snare mucosectomy in the esophagus without any additional equipment: a simple technique for resection of flat early cancer. Endoscopy 1997; 29: 380-383 [PMID: 9270919 DOI: 10.1055/s-2007-1004219]

75 Tanaka S, Oka S, Chayama K. Colorectal endoscopic submucosal dissection: present status and future perspective, including its differentiation from endoscopic mucosal resection. J Gastroenterol 2008; 43: 641-651 [PMID: 18807125 DOI: 10.1007/s00535-008-2223-4]

76 Repici A, Pellicano R, Strangio G, Danese S, Fagoonee S, Malesci A. Endoscopic mucosal resection for early colorectal neoplasia: pathologic basis, procedures, and outcomes. Dis Colon Rectum 2009; 52: 1502-1515 [PMID: 19617768 DOI: 10.1007/DCR.0b013e3181a74d9b]

77 Kitajima K, Fujimori T, Fujii S, Takeda J, Ohkura Y, Kawamata H, Kumamoto T, Ishiguro S, Kato Y, Shimoda T, Iwashita A, Ajioka Y, Watanabe H, Watanabe T, Muto T, Nagasako K. Correlations between lymph node metastasis and depth of submucosal invasion in submucosal invasive colorectal carcinoma: a Japanese collaborative study. J Gastroenterol 2004; 39: 534-543 [PMID: 15235870 DOI: 10.1007/s00535-004-1339-4]

78 Moss A, Bourke MJ, Williams SJ, Hourigan LF, Brown G, Tam W, Singh R, Zanati S, Chen RY, Byth K. Endoscopic mucosal resection outcomes and prediction of submucosal cancer from advanced colonic mucosal neoplasia. Gastroenterology 2011; 140: 1909-1918 [PMID: 21392504 DOI: 10.1053/j.gastro.2011.02.062]

79 Brooker JC, Saunders BP, Shah SG, Thapar CJ, Suzuki N, Williams CB. Treatment with argon plasma coagulation reduces recurrence after piecemeal resection of large sessile colonic polyps: a randomized trial and recommendations. Gastrointest Endosc 2002; 55: 371-375 [PMID: 11868011 DOI: 10.1067/mge.2002.121597]

80 Seitz U, Bohnacker S, Seewald S, Thonke F, Soehendra N. Long-term results of endoscopic removal of large colorectal adenomas. Endoscopy 2003; 35: S41-S44 [PMID: 12929053 DOI: 10.1055/s-2003-41535]

81 Lin OS. Clinical update: postpolypectomy colonoscopy surveillance. Lancet 2007; 370: 1674-1676 [PMID: 18022025 DOI: 10.1016/S0140-6736(07)61707-3]

82 Arebi N, Swain D, Suzuki N, Fraser C, Price A, Saunders BP. Endoscopic mucosal resection of 161 cases of large sessile or flat colorectal polyps. Scand J Gastroenterol 2007; 42: 859-866 [PMID: 17558911 DOI: 10.1080/00365520601137280]

83 Ferrara F, Luigiano C, Ghersi S, Fabbri C, Bassi M, Landi P, Polifemo AM, Billi P, Cennamo V, Consolo P, Alibrandi A, D'Imperio N. Efficacy, safety and outcomes of 'inject and cut' endoscopic mucosal resection for large sessile and flat colorectal polyps. Digestion 2010; 82: 213-220 [PMID: 20588036 DOI: 10.1159/000284397]

84 Luigiano C, Consolo P, Scaffidi MG, Strangio G, Giacobbe G, Alibrandi A, Pallio S, Tortora A, Melita G, Familiari L. Endoscopic mucosal resection for large and giant sessile and flat colorectal polyps: a single-center experience with long-term follow-up. Endoscopy 2009; 41: 829-835 [PMID: 19750448 DOI: 10.1055/s-0029-1215091]

85 Tanaka S, Haruma K, Oka S, Takahashi R, Kunihiro M, Kitadai Y, Yoshihara M, Shimamoto F, Chayama K. Clinicopathologic features and endoscopic treatment of superficially spreading colorectal neoplasms larger than 20 mm. Gastrointest Endosc 2001; 54: 62-66 [PMID: 11427843 DOI: 10.1067/mge.2001.115729]

86 Saito Y, Fukuzawa M, Matsuda T, Fukunaga S, Sakamoto T, Uraoka T, Nakajima T, Ikehara H, Fu KI, Itoi T, Fujii T. Clinical outcome of endoscopic submucosal dissection versus endoscopic mucosal resection of large colorectal tumors as determined by curative resection. Surg Endosc 2010; 24: 343-352 [PMID: 19517168 DOI: 10.1007/s00464-009-0562-8]

87 Iishi H, Tatsuta M, Iseki K, Narahara H, Uedo N, Sakai N, Ishikawa H, Otani T, Ishiguro S. Endoscopic piecemeal resection with submucosal saline injection of large sessile colorectal polyps. Gastrointest Endosc 2000; 51: 697-700 [PMID: 10840302 DOI: 10.1067/mge.2000.104652]

88 Deprez PH, Bergman JJ, Meisner S, Ponchon T, Repici A, Dinis-Ribeiro M, Haringsma J. Current practice with endoscopic submucosal dissection in Europe: position statement from a panel of experts. Endoscopy 2010; 42: 853-858 [PMID: 20623442 DOI: 10.1055/s-0030-1255563.]

89 Hotta K, Oyama T, Shinohara T, Miyata Y, Takahashi A, Kitamura Y, Tomori A. Learning curve for endoscopic submucosal dissection of large colorectal tumors. Dig Endosc 2010; 22: 302-306 [PMID: 21175483 DOI: 10.1111/j.1443-1661.2010.01005.x]

90 Sakamoto T, Saito Y, Fukunaga S, Nakajima T, Matsuda T. Learning curve associated with colorectal endoscopic submucosal dissection for endoscopists experienced in gastric endoscopic submucosal dissection. Dis Colon Rectum 2011; 54: 1307-1312 [PMID: 21904147 DOI: 10.1097/DCR.0b013e3182282ab0]

91 Probst A, Golger D, Anthuber M, Märkl B, Messmann H. Endoscopic submucosal dissection in large sessile lesions of the rectosigmoid: learning curve in a European center. Endoscopy 2012; 44: 660-667 [PMID: 22528673 DOI: 10.1055/s-0032-1309403]

92 Tanaka S, Oka S, Kaneko I, Hirata M, Mouri R, Kanao H, Yoshida S, Chayama K. Endoscopic submucosal dissection for colorectal neoplasia: possibility of standardization. Gastrointest Endosc 2007; 66: 100-107 [PMID: 17591481 DOI: 10.1016/j.gie.2007.02.032]

93 Saito Y, Uraoka T, Matsuda T, Emura F, Ikehara H, Mashimo Y, Kikuchi T, Fu KI, Sano Y, Saito D. Endoscopic treatment of large superficial colorectal tumors: a case series of 200 endoscopic submucosal dissections (with video). Gastrointest Endosc 2007; 66: 966-973 [PMID: 17524403 DOI: 10.1016/j.gie.2007.02.053]

94 Fujishiro M, Yahagi N, Kakushima N, Kodashima S, Muraki Y, Ono S, Yamamichi N, Tateishi A, Oka M, Ogura K, Kawabe T, Ichinose M, Omata M. Outcomes of endoscopic submucosal dissection for colorectal epithelial neoplasms in 200 consecutive cases. Clin Gastroenterol Hepatol 2007; 5: 678-83; quiz 645 [PMID: 17466600 DOI: 10.1016/j.cgh.2007.01.006]

95 Tamegai Y, Saito Y, Masaki N, Hinohara C, Oshima T, Kogure E, Liu Y, Uemura N, Saito K. Endoscopic submucosal dissection: a safe technique for colorectal tumors. Endoscopy 2007; 39: 418-422 [PMID: 17516348 DOI: 10.1055/s-2007-966427]

96 Yoshida N, Naito Y, Sakai K, Sumida Y, Kanemasa K, Inoue K, Morimoto Y, Konishi H, Wakabayashi N, Kokura S, Yagi N, Yanagisawa A, Yoshikawa T. Outcome of endoscopic submucosal dissection for colorectal tumors in elderly people. Int J Colorectal Dis 2010; 25: 455-461 [PMID: 19921221 DOI: 10.1007/s00384-009-0841-9]

97 Kim MN, Kang JM, Yang JI, Kim BK, Im JP, Kim SG, Jung HC, Song IS, Kim JS. Clinical features and prognosis of early colorectal cancer treated by endoscopic mucosal resection. J Gastroenterol Hepatol 2011; 26: 1619-1625 [PMID: 21517966 DOI: 10.1111/j.1440-1746.2011.06749.x]

98 Nishiyama H, Isomoto H, Yamaguchi N, Fukuda E, Ikeda K, Ohnita K, Mizuta Y, Nakamura T, Nakao K, Kohno S, Shikuwa S. Endoscopic submucosal dissection for colorectal epithelial neoplasms. Dis Colon Rectum 2010; 53: 161-168 [PMID: 20087091 DOI: 10.1007/DCR.0b013e3181b78cb6]

99 Yamamoto H, Kawata H, Sunada K, Sasaki A, Nakazawa K, Miyata T, Sekine Y, Yano T, Satoh K, Ido K, Sugano K. Successful en-bloc resection of large superficial tumors in the stomach and colon using sodium hyaluronate and small-caliber-tip transparent hood. Endoscopy 2003; 35: 690-694 [PMID: 12929067 DOI: 10.1055/s-2003-41516]

100 Yoshida N, Yagi N, Naito Y, Yoshikawa T. Safe procedure in endoscopic submucosal dissection for colorectal tumors focused on preventing complications. World J Gastroenterol 2010; 16: 1688-1695 [PMID: 20379999 DOI: 10.3748/wjg.v16.i14.1688]

101 Matsumoto A, Tanaka S, Oba S, Kanao H, Oka S, Yoshihara M, Chayama K. Outcome of endoscopic submucosal dissection for colorectal tumors accompanied by fibrosis. Scand J Gastroenterol 2010; 45: 1329-1337 [PMID: 20626303 DOI: 10.3109/00365521.2010.495416]

102 Uraoka T, Kawahara Y, Kato J, Saito Y, Yamamoto K. Endoscopic submucosal dissection in the colorectum: present status and future prospects. Dig Endosc 2009; 21 Suppl 1: S13-S16 [PMID: 19691725 DOI: 10.1111/j.1443-1661.2009.00863.x]

103 Isomoto H, Nishiyama H, Yamaguchi N, Fukuda E, Ishii H, Ikeda K, Ohnita K, Nakao K, Kohno S, Shikuwa S. Clinicopathological factors associated with clinical outcomes of endoscopic submucosal dissection for colorectal epithelial neoplasms. Endoscopy 2009; 41: 679-683 [PMID: 19670135 DOI: 10.1055/s-0029-1214979]

104 Singh R, Neo EN, Nordeen N, Shanmuganathan G, Ashby A, Drummond S, Nind G, Murphy E, Luck A, Tucker G, Tam W. Carbon dioxide insufflation during colonoscopy in deeply sedated patients. World J Gastroenterol 2012; 18: 3250-3253 [PMID: 22783048 DOI: 10.3748/wjg.v18.i25.3250]

105 Park SY, Jeon SW. Acute intestinal obstruction after endoscopic submucosal dissection: report of a case. Dis Colon Rectum 2008; 51: 1295-1297 [PMID: 18536969 DOI: 10.1007/s10350-008-9344-y]

106 Oka S, Tanaka S, Kanao H, Ishikawa H, Watanabe T, Igarashi M, Saito Y, Ikematsu H, Kobayashi K, Inoue Y, Yahagi N, Tsuda S, Simizu S, Iishi H, Yamano H, Kudo SE, Tsuruta O, Tamura S, Saito Y, Cho E, Fujii T, Sano Y, Nakamura H, Sugihara K, Muto T. Current status in the occurrence of postoperative bleeding, perforation and residual/local recurrence during colonoscopic treatment in Japan. Dig Endosc 2010; 22: 376-380 [PMID: 21175503 DOI: 10.1111/j.1443-1661.2010.01016.x]

107 Yan J, Trencheva K, Lee SW, Sonoda T, Shukla P, Milsom JW. Treatment for right colon polyps not removable using standard colonoscopy: combined laparoscopic-colonoscopic approach. Dis Colon Rectum 2011; 54: 753-758 [PMID: 21552062 DOI: 10.1007/DCR.0b013e3182108289]

108 Wood JJ, Lord AC, Wheeler JM, Borley NR. Laparo-endoscopic resection for extensive and inaccessible colorectal polyps: a feasible and safe procedure. Ann R Coll Surg Engl 2011; 93: 241-245 [PMID: 21477440 DOI: 10.1308/003588411X565978]

109 Wilhelm D, von Delius S, Weber L, Meining A, Schneider A, Friess H, Schmid RM, Frimberger E, Feussner H. Combined laparoscopic-endoscopic resections of colorectal polyps: 10-year experience and follow-up. Surg Endosc 2009; 23: 688-693 [PMID: 19169747 DOI: 10.1007/s00464-008-0282-5]

P-Reviewer Probst A         S-Editor Wen LL             L-Editor                  E-Editor

Table 1 Factors associated with adenoma detection

| Variable | Association |
| --- | --- |
| Withdrawal Time < 6 min | Worse |
| Sub-optimal bowel preparation | Worse |
| Patient anatomy | Variable |
| Experience of endoscopist | Variable (mostly worse with early) |
| Afternoon endoscopy | Worse |
| Flat adenomas | Worse |
| < 1cm | Worse |
| Narrow band imaging | Variable data1 |
| Chromoendoscopy | Variable data1 |

1Compared to traditional white light colonoscopy.